## Slide 1
Q-Hack India 2026
Team Name:
Team Lead Name:
Track:
Problem Statement title:
lwyrup
Neelagiri Karthikeya
Quantum Security & Cryptography
Detecting Faked Quantum Cloud Jobs

## Slide 2
Q-Hack India 2026
Problem
■ Quantum time is rented over the cloud, often through resellers and marketplaces, and billed per second of QPU time.
■ Customers only get back bitstrings. There is no way to check that the job actually ran on quantum hardware.
■ IBM publishes every device's calibration daily (gate and readout error rates). Anyone can build a realistic noisy simulator from it.
■ The attack: a dishonest provider runs small jobs on a laptop simulator built from that public data, returns believably noisy results, and still bills for QPU time.

## Slide 3
Q-Hack India 2026
Why It Matters
■ Who is affected: researchers, startups and students paying for QPU time or spending limited free credits.
■ Silent corruption: faked results poison benchmarks, papers and error-mitigation studies, and nobody notices.
■ Trust in the execution layer is a security problem as quantum access moves to resellers and multi-vendor marketplaces.
■ The gap: prior device-fingerprinting work (2025) argues forgery is hard, but only for circuits too large to simulate, and never tests a real forger. Small, simulable jobs, common today, are unprotected.

## Slide 4
Q-Hack India 2026
Proposed Solution
GhostQPU: proof that your quantum job really ran on a quantum computer.
■ Hidden canaries: 30 small test circuits ride inside each 34-circuit job, compiled and shuffled so the provider can't tell which are tests.
■ Physics a simulator leaves out: canaries trigger coherent error build-up, neighbor crosstalk, context-dependent readout and drift.
■ Detector: turns canary results into a verdict (Genuine, Forged or Inconclusive). One command: python -m ghostqpu verify <job>.
■ We built the attacker too: a Forger using the exact calibration live when each job ran, plus a stronger Forger that learns hardware effects.
■ Disguised canaries: a random circuit followed by its reverse looks like customer work, yet still exposes the Forger.

## Slide 5
Q-Hack India 2026
Why Quantum?
■ The evidence is quantum: the fingerprint is the physical noise of the real chip, which only exists on quantum hardware.
■ Canaries amplify it: 128 repeated X gates turn tiny coherent over-rotations into a 91% error on ibm_kingston, where the Forger predicts 2%.
■ Why calibration can't fake it: published calibration describes each gate on its own with average error rates. Real qubits have coherent, correlated, time-varying noise.
■ Real hardware: three 156-qubit IBM Heron devices (ibm_marrakesh, ibm_fez, ibm_kingston) through Qiskit Runtime, on the free plan.

## Slide 6
Q-Hack India 2026
Implementation and Architecture
Pipeline
■ Calibration snapshot → Batch builder (canaries + workload, shuffled) → IBM QPU (Qiskit Runtime Sampler, twirling and dynamical decoupling off) → Collect, plus the calibration live at execution → Forger (Qiskit Aer + that calibration) → Signature (12 features per time chunk) → Detector → Verdict
■ Quantum components: 3 canary families on 4 isolated qubit pairs at transpiler level 0, plus CNOT and disguised mirror pilot circuits.
■ Classical components: Python, Qiskit 2.5, Qiskit Aer, scikit-learn logistic regression, Next.js + three.js site deployed on GitHub Pages.
■ Engineering: CLI (submit / collect / verify / evaluate / null-test), 36 automated tests, hardware-simulator bit-order parity test, seeded Forger.

## Slide 7
Q-Hack India 2026
Minimal Prototype
■ Working end-to-end tool: python -m ghostqpu submit / collect / verify / evaluate / null-test.
■ Real hardware runs: 23 jobs on ibm_marrakesh, ibm_fez and ibm_kingston over 18 calibration cycles and 4 days, each with a forged twin.
■ Live site: jacklachan.github.io/GhostQPU, a six-chapter story with a console that replays real IBM jobs for a blind verdict.
■ Interactive: a Bloch sphere driven by measured data, and a lab where you play the Forger against the real frozen Detector.
■ Pilots on hardware: CNOT canaries, disguised mirror canaries and real 250-shot cost checks on all three machines.
■ Open: every run, calibration snapshot and research note is in the GitHub repo.

## Slide 8
Q-Hack India 2026
Results / Validation
■ Frozen Detector, scored blind: 46 of 46 later jobs correct (23 real, 23 forged), 18 cycles, 3 machines.
■ Held out by cycle: AUC 1.00, 50 of 50 over 19 cycles. Trained only on earlier days: 46 of 46.
■ Null test: simulator vs Forger scores AUC 0.52 (chance), so it detects physics, not formatting.
■ Cost: 1.5 QPU seconds of canaries still calls all 50 jobs right.
■ Why AUC is 1.00: public calibration has no coherent error, so the Forger is 2-4% wrong where hardware is 30-90%.
■ Smarter Forger: learning from a real job fooled the frozen Detector 12/13; retrained, caught 12/13.
Canary | Real hardware | Forger
Error after 128 X gates (kingston) | 91% | 2%
Idle-qubit shift from neighbor (fez) | 30% | 4%
Disguised canary all-zero rate (marrakesh) | 76% | 88%

## Slide 9
Q-Hack India 2026
Roadmap
■ Done since 10 Oct: cross-day and cross-backend validation (ibm_fez, ibm_kingston), 85% lower canary cost, disguised canaries.
■ Canary-aware forger: our stronger Forger fooled the original Detector; next, require evidence from two canary families.
■ CNOT canary family: 73% vs 10% on marrakesh qubits 107-108, detected on 13 of 16 pairs; make it a production family.
■ Customer SDK: a drop-in wrapper that injects canaries into every job and returns a signed verification report.
■ Scale the evidence: weeks of daily runs and more cloud providers to tighten the false-alarm bound.

## Slide 10
Q-Hack India 2026
References and Sources
■ Prior work: Martina et al. 2022; Pirnay et al. 2022 (forged single-qubit fingerprints); Mutolo et al. 2025 (fingerprinting, no tested forger); Wu, Hu, Li 2024 (catches device substitution, not simulation).
■ IBM Quantum Platform: Open plan, Heron backends and published calibration data (quantum.cloud.ibm.com).
■ Software: Qiskit, Qiskit Aer, Qiskit IBM Runtime, scikit-learn, Next.js, three.js.
■ Our code and site: github.com/Karthikeya47/GhostQPU · jacklachan.github.io/GhostQPU (all implementation is the team's own work).
■ Team lwyrup: Neelagiri Karthikeya (lead), L Mohit Jain, Tanvi Jain, Aditi Gorti.